## Slide 1: SPH3U Simple Circuit
Start with a simple electric circuit, with a 6.0 V battery source and a single 10 W resistor
VT= 6.0 V
IT=
RT = 10 W
Resistor
V1=
I1=
R1=10 W
Getting the H.O.T.S. for Physics
a Dave Doucette Production
+3.0V
-3.0V
The 6.0 V battery has 2 terminals:
+3.0 V and -3.0 V.
The voltage (potential difference)
between the two terminals is 6.0 V.

## Slide 2: SPH3U Simple Circuit
Start with a simple electric circuit, with a 6.0 V battery source and a single 10 W resistor
VT= 6.0 V
IT=
RT = 10 W
Resistor
V1=
I1=
R1=10 W
Getting the H.O.T.S. for Physics
a Dave Doucette Production
+3.0V
-3.0V
The 6.0 V battery has 2 terminals:
+3.0 V and -3.0 V
+3.0V
+3.0V
+3.0V
This conducting wire
has a voltage of +3.0V
This conducting wire has a voltage of -3.0 V
-3.0V
-3.0V
-3.0V

## Slide 3: SPH3U Simple Circuit
Start with a simple electric circuit, with a 6.0 V battery source and a single 10 W resistor
VT= 6.0 V
IT=
RT = 10 W
Resistor
V1=
I1=
R1=10 W
Getting the H.O.T.S. for Physics
a Dave Doucette Production
+3.0V
-3.0V
The 6.0 V battery has 2 terminals:
+3.0 V and -3.0 V
+3.0V
+3.0V
+3.0V
This conducting wire
has a voltage of +3.0V
This conducting wire has a voltage of -3.0 V
-3.0V
-3.0V
-3.0V
6.0 V/10 W = 0.60 A
6.0 V
0.60 A

## Slide 4: SPH3U Series Circuit
Now we add a second 10 W resistor in series
VT= 6.0 V
IT=
RT = 20 W
Resistor 1
V1=
I1=
R1=10 W
Getting the H.O.T.S. for Physics
a Dave Doucette Production
+3.0V
-3.0V
+3.0V
This conducting wire still has a voltage of -3.0 V
-3.0V
-3.0V
-3.0V
This conducting wire
has a voltage of +3.0V
Resistor 2
V1=
I1=
R1=10 W
+3.0V
6.0 V/20 W = 0.30 A
0.30 A
0.30 A
3.0 V
3.0 V
This conducting wire is midway between +3.0 V and -3.0 V, ie, 0.0 V.
0.0 V

## Slide 5: SPH3U Series Circuit
Let us look at this circuit again – in terms of the potential differences across the source and the resistors
Getting the H.O.T.S. for Physics
a Dave Doucette Production
+3.0V
-3.0V
+3.0V
-3.0V
-3.0V
-3.0V
+3.0V
0.0 V
The voltage across the source is 6.0 V
The voltage across resistor 1 is 3.0 V
The voltage across resistor 2 is 3.0 V
The sum of the potential differences across the resistors equals the potential difference across the source. This occurs due to the distribution of surface charge.
3.0 V
3.0 V
6.0 V
+
=

## Slide 6: SPH3U Series Circuit
Now we add a third 10 W resistor in series
VT= 6.0 V
IT=
RT = 30 W
Resistor 1
V1=
I1=
R1=10 W
Getting the H.O.T.S. for Physics
a Dave Doucette Production
+3.0V
-3.0V
+3.0V
This conducting wire still has
a voltage of -3.0 V
-3.0V
-3.0V
This conducting wire
Still has a voltage of +3.0V
Resistor 2
V1=
I1=
R1=10 W
+3.0V
6.0 V/30 W = 0.20 A
Resistor 3
V1=
I1=
R1=10 W
2.0 V
2.0 V
2.0 V
0.20 A
0.20 A
0.20 A
This conducting wire
has a voltage of +1.0V
This conducting wire
has a voltage of -1.0V
+1.0V
-1.0V

## Slide 7: SPH3U Series Circuit
Getting the H.O.T.S. for Physics
a Dave Doucette Production
+3.0V
-3.0V
+3.0V
-3.0V
-3.0V
+3.0V
+1.0V
-1.0V
Let us look at this circuit again – in terms of the potential differences across the source and the resistors
The voltage across the source is 6.0 V
The voltage across resistor 1 is 2.0 V
The voltage across resistor 2 is 2.0 V
The voltage across resistor 3 is 2.0 V
2.0 V
2.0 V
2.0 V
+
+
=
6.0 V

## Slide 8: Part 2
Potential Difference
&
Parallel Circuits

## Slide 9: SPH3U Parallel Circuit
Start with a 12 V battery source and two 8.0 W resistors, in a parallel circuit:
VT= 12 V
IT= 12V / 4.0 W = 3.0 A
RT = _______1_____ = 4.0 W
1/8.0 + 1/8.0
Resistor 1
V1=
I1=
R1=8.0 W
Getting the H.O.T.S. for Physics
a Dave Doucette Production
+6.0 V
-6.0 V
The 12 V battery has 2 terminals:
+6.0 V and -6.0 V.
The voltage (potential difference)
between the two terminals is 12 V.
Resistor 2
V2=
I2=
R2=8.0 W
+6.0 V
These conducting wires have
a voltage of +6.0 V
These conducting wires have
a voltage of +6.0 V
+6.0 V
+6.0 V
-6.0 V
-6.0 V
-6.0 V
12 V
12 V
1.5 A
1.5 A